## Slide 1: Data Reduction Goals
From a series of diffraction images, obtain a file containing the intensity (Ihkl) and standard deviation (s(Ihkl)) for each reflection, hkl.
H K L I s
0 0 4 3295.4 174.0
0 0 8 482.1 28.7
0 0 12 9691.0 500.7
0 0 16 1743.9 67.4
0 0 20 5856.0 221.0
0 0 24 14066.5 436.2
0 0 28 9936.3 311.7
0 0 36 8409.8 273.4
0 0 40 790.5 32.8
0 0 44 103.4 18.4
. . . . .
. . . . .
. . . . .
37 7 0 28.5 16.2
37 7 1 110.1 10.9
37 7 2 337.4 13.3
37 7 3 98.5 10.6
37 7 4 25.9 10.7
Set of 720 images.
Each image covers 0.5°
Final intensities
Index
Integrate
Merge
13,000 Mb
2 Mb
720
719
718
717
716

## Slide 2: Determine the space group of the crystal by process of elimination.
System | Bravais lattice | Point group | 65 Chiral Space Groups |  |  |  |  | 
Triclinic | P | 1 | P1 |  |  |  |  | 
Monoclinic | P | 2 | P2 | P21 |  |  |  | 
 | C |  | C2 |  |  |  |  | 
Orthorhombic | P | 222 | P222 | P2221 | P21212 | P212121 |  | 
 | C |  | C2221 | C222 |  |  |  | 
 | F |  | F222 |  |  |  |  | 
 | I |  | I222 | I212121 |  |  |  | 
Tetragonal | P | 4 | P4 | P41 | P42 | P43 |  | 
 | I |  | I4 | I41 |  |  |  | 
 | P | 422 | P422 | P4212 | P4122 | P41212 | P4222 | P42212
 |  |  |  |  | P4322 | P43212 |  | 
 | I |  | I422 | I4122 |  |  |  | 
Trigonal/ Rhombo-hedral | P | 3 | P3 | P31 | P32 |  |  | 
 | R |  | R3 |  |  |  |  | 
 | P | 32 | P312 | P321 | P3112 | P3121 | P3212 | P3221
 | R |  | R32 |  |  |  |  | 
Hexagonal | P | 6 | P6 | P61 | P62 | P63 | P64 | P65
 |  | 622 | P622 | P6122 | P6222 | P6322 | P6422 | P6522
Cubic | P | 23 | P23 | P213 |  |  |  | 
 | F |  | F23 |  |  |  |  | 
 | I |  | I23 | I213 |  |  |  | 
 | P | 432 | P432 | P4232 | P4332 | P4132 |  | 
 | F |  | F432 | F4132 |  |  |  | 
 | I |  | I432 | I4132 |  |  |  | 
2
3
4
65 chiral space groups: ProK is made of L-amino acids. Only 65 of the 230 space groups support chiral motifs.
14 Bravais lattices: find best fit of to diffraction pattern.
Point group symmetry: find best fit to reflection intensity pattern. Rotational symmetry in the diffraction pattern infers rotational symmetry in the crystal.
Pure rotation or screw axis: discern by examining systematic absences.
1

## Slide 3: Learn how to judge the quality of data collection statistics.

## Slide 4: Indexing
2,0,0
3,0,-1
4,0,-2
5,0,-3
5,0,-4
5,0,-5
4,0,-6
3,0,-7
2,0,-7
1,0,-8
0,0,-8
-1,0,-8
Assign an h,k,l coordinate to each reflection of the first image.
Indices h,k,l are coordinates of the reflections, analogous to how atom positions are described by coordinates x,y,z.

## Slide 5: Understand the relationship between the crystal, the reciprocal lattice and the diffraction pattern
Unit cell lengths a, b, c
Atom coordinates x, y, z
Reciprocal cell lengths a*, b*, c*
Reflection coordinates h, k, l
Goal of data reduction is to measure intensity at each lattice point, h,k,l.
Crystal
Reciprocal Lattice
Fourier
Transform
Diffraction Pattern
A 2D projection of a 3D reciprocal lattice
Diffraction
Experiment
Notes: In our diffraction experiment, we are trying to measure the Fourier transform of the crystal. The Fourier transform of a crystal is a reciprocal lattice where each lattice point contains a spot with index hkl and amplitude F, corresponding to the transform of the motif. We measure intensity. Fhkl= SQRT(Ihkl)

## Slide 6
Crystal
X-ray beam
Reciprocal
lattice
Ewald’s sphere of reflection
Detector
Diffracted rays
Simulated Data Collection

## Slide 7: Indexing is conceptually simple with precession photographs
Provides an undistorted view of one plane of the reciprocal lattice
Taken in early 1990s.

## Slide 8: Buerger Precession Camera

## Slide 9: How to Index by Inspection
Recall that spots are arrayed on a reciprocal lattice.
Count how many steps the given reflection is displaced from the origin.
  h=Number of steps of a*.
  k=Number of steps of b*.
  l=Number of steps of c*.

## Slide 10: Index the reflection circled in cyan.
What pieces of information are required to index this reflection?
1) Define lattice points
2) Define a*,b*, c* direction & length
3) Locate origin.

## Slide 11: Mark lattice points with red circles.
Note the spacing between reflections is periodic.
Draw evenly spaced lines through the spots to define the spacings a* & b*

## Slide 12: Draw evenly spaced lines thru spots
Lines must intercept every spot on film.
Choose widest possible spacing that accounts for all spots.

## Slide 13: Draw evenly spaced lines thru spots
A wider reciprocal spacing gives smaller (better) real cell spacing.
Draw another set of evenly spaced lines at 90° or 120°, if possible.

## Slide 14: This 2D net represents one plane of the reciprocal lattice

## Slide 15: Weak reflections not detected previously can be predicted at lattice points. Note: we didn’t need to identify the position of every spot to get the lattice.

## Slide 16: Locate origin of reciprocal lattice
Origin is located where direct x-ray beam intercepts image. To see it, briefly remove beam-stop.

## Slide 17: Origin is defined. Now, label a* & b*
a*
b*
What is the index of the spot?
a*
b*

## Slide 18: Reflection h,k,l is 3,8,0
a*
b*
a*
a*
a*
b*
b*
b*
b*
b*
b*
b*
b*
3rd column on the right side of the origin.
8th row above the origin

## Slide 19: Which Bravais Lattice fits this pattern?
a*
b*
a*
b*
a* and b* have the same length.
They are perpendicular to each other.

## Slide 20: Which Bravais Lattice fits this pattern?
a=b and g=90°

## Slide 21: Next, index spots on an oscillation image.
This is easy!
But, what about this?

## Slide 22: Challenges in indexing an oscillation image
Orientation of reciprocal cell vectors a*, b*, c* are not aligned with film edges— the orientation of the crystal in the loop is arbitrary.
Can’t see symmetry in the pattern..
Multiple planes of the reciprocal lattice are in view, not just a single plane.
The oscillation image is a 2D projections of a 3D lattice—a dimension of depth is lost.
Oscillation image.

## Slide 23: 2D diffraction image is a projection from a 3D reciprocal lattice.
detector
In an undistorted view of the reciprocal lattice, recorded reflections would reside on the surface of a sphere, not a plane.
a*
c*
b*

## Slide 24: A distortion-corrected representation of the reflections a single image reveals all 6 unit cell parameters

## Slide 25: Restored depth of the diffraction pattern is evident from an orthogonal view

## Slide 26: Need a program that can automatically identify spot positions, interpret crystal orientation, and unit cell dimensions.

## Slide 27: Automatic indexing algorithm explained
Kabsch, W. (1988a) Automatic Indexing of Rotation Diffraction Patterns. J. Appl. Cryst. 21, 67–72.

## Slide 28: Locate spot positions with COLSPOT
!====================== JOB CONTROL PARAMETERS ===============================
JOB= ALL !XYCORR INIT COLSPOT IDXREF DEFPIX INTEGRATE CORRECT
!====================== GEOMETRICAL PARAMETERS ===============================
ORGX=1506.23 ORGY=1503.91 !Detector origin (pixels). Calibrated by DC 03/01/2019
DETECTOR_DISTANCE=-74 !(mm)
ROTATION_AXIS= 0.0 1.0 0.0
OSCILLATION_RANGE=0.5 !degrees (>0)
X-RAY_WAVELENGTH=1.5418 !Angstrom
INCLUDE_RESOLUTION_RANGE=100.0 1.4
!==================== SELECTION OF DATA IMAGES ==============================
NAME_TEMPLATE_OF_DATA_FRAMES=i/prok_gd_angela????.osc DIRECT RAXIS
DATA_RANGE= 1 720 !First and last diffraction images collected
BACKGROUND_RANGE=1 4 !First and last data image for background
SPOT_RANGE= 1 10 !First and last data image number for finding spots
SPOT_RANGE= 171 180 !First and last data image number for finding spots
!============================================================================
XDS.INP file specifies automatic indexing instructions

## Slide 29
001 002 003 004 005
006 007 008 009 010
171 172 173 174 175
176 177 178 179 180

## Slide 30
001 002 003 004 005
006 007 008 009 010
171 172 173 174 175
176 177 178 179 180

## Slide 31
001 002 003 004 005
006 007 008 009 010
171 172 173 174 175
176 177 178 179 180

## Slide 32: SPOT.XDS
Spot position intens-
X Y phi ity
1504.01 1378.41 173.66 4537.
1526.45 1409.21 172.51 4485.
1499.41 1575.97 3.49 4395.
1499.77 1247.89 175.02 4004.
1482.28 1251.21 175.64 3430.
1460.42 1235.69 178.37 3111.
1515.65 1235.92 4.29 2099.
1516.82 1246.26 175.68 2043.
1494.83 1721.10 5.95 2002.
1460.63 1751.46 173.68 1935.
1496.21 1889.74 173.68 1869.
1536.70 1371.16 178.43 1775.
1509.20 1578.62 5.50 1705.
1520.18 1374.85 177.59 1695.
1480.15 1261.73 3.54 1664.
1471.50 1863.84 7.45 1649.
1470.76 1382.48 171.31 1644.
1500.62 1680.58 6.31 1643.
1563.73 1808.92 2.41 1613.
1460.22 1420.42 171.54 1604.
1472.21 1173.36 7.24 1589.
1510.04 1148.16 5.10 1539.
1448.42 1257.31 173.54 1534.
1511.90 1318.37 173.95 1452.
1560.73 1612.72 178.46 1448.
1532.31 1222.84 173.71 1417.
1491.13 1159.51 6.08 1363.
1551.09 1095.47 176.33 1360.
1574.56 1223.31 1.50 1278.
1510.01 1802.89 5.71 1266.
1548.82 1523.06 5.03 1213.
1426.96 1242.19 174.81 1210.
NUMBER OF DIFFRACTION SPOTS LOCATED 25118
IGNORED BECAUSE OF SPOT CLOSE TO UNTRUSTED REGION 13
WEAK SPOTS OMITTED 22
NUMBER OF DIFFRACTION SPOTS ACCEPTED 25083

## Slide 33: Reciprocal Lattice 3D reconstruction using images 1-10 & 171-180
001
001, 002
001, 002, 003
001, 002, 003, 004
001, 002, 003, 004, 005
001, 002, 003, 004, 005, 006
001, 002, 003, 004, 005, 006, 007
001, 002, 003, 004, 005, 006, 007, 008
001, 002, 003, 004, 005, 006, 007, 008, 009
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175,
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177, 178
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177, 178, 179
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177, 178, 179, 180
001
001, 002
001, 002, 003
001, 002, 003, 004
001, 002, 003, 004, 005
001, 002, 003, 004, 005, 006
001, 002, 003, 004, 005, 006, 007
001, 002, 003, 004, 005, 006, 007, 008
001, 002, 003, 004, 005, 006, 007, 008, 009
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175,
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177, 178
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177, 178, 179
001, 002, 003, 004, 005, 006, 007, 008, 009, 010
171, 172, 173, 174, 175, 176, 177, 178, 179, 180
Spindle axis
Spindle axis
25083 spots

## Slide 34: Draw vectors between reciprocal lattice points. For simplicity, only points from image 8 are shown.

## Slide 35: Vectors of same length & direction are grouped together
65 vectors like this:

## Slide 36: Vectors of same length & direction are grouped together
53 vectors like this:

## Slide 37: Algorithm for best choice of a*, b*, c*
Difference vector clusters are accumulated in a 3D histogram. These vectors represent all candidate reciprocal lattice vectors. For example:
Choose the shortest three linear independent real-space lattice vectors forming a right-handed set.
# COORDINATES OF VECTOR CLUSTER FREQUENCY CLUSTER INDICES
1 -0.0026247 0.0170582-0.0027500 2025. 0.99 -0.00 -0.99
2 -0.0060520-0.0130311 0.0026847 1878. -1.00 0.00 0.01
3 -0.0086356 0.0040538-0.0000834 1832. -0.00 -0.00 -0.99
4 -0.0034720-0.0301176 0.0054258 1536. -1.99 0.00 1.00
5 -0.0052358 0.0342473-0.0054914 1414. 2.00 -0.00 -1.99
6 -0.0015319 0.0195839 0.0114708 1380. 1.00 0.99 -1.00
7 0.0045649 0.0325816 0.0088457 1372. 2.00 1.00 -1.00
. . . . . . . .
60 0.0044282-0.0816564 0.0136375 685. -5.00 -0.00 4.00

## Slide 38: Choose the lattice of highest symmetry and quality of fit<10
LATTICE- BRAVAIS- QUALITY UNIT CELL CONSTANTS (ANGSTROEM & DEGREES)
CHARACTER LATTICE OF FIT a b c alpha beta gamma
* 44 aP 0.0 68.2 68.4 102.9 90.1 90.2 90.1
* 31 aP 0.7 68.2 68.4 102.9 90.1 89.8 89.9
* 33 mP 1.4 68.2 68.4 102.9 90.1 90.2 90.1
* 34 mP 3.2 68.2 102.9 68.4 90.1 90.1 90.2
* 35 mP 3.3 68.4 68.2 102.9 90.2 90.1 90.1
* 32 oP 3.9 68.2 68.4 102.9 90.1 90.2 90.1
* 14 mC 5.5 96.5 96.7 102.9 89.9 90.2 89.8
* 10 mC 6.3 96.5 96.7 102.9 90.1 90.2 90.2
* 13 oC 6.9 96.5 96.7 102.9 89.9 90.2 89.8
* 11 tP 7.6 68.2 68.4 102.9 90.1 90.2 90.1
37 mC 248.2 216.5 68.2 68.4 90.1 90.1 71.8
36 oC 248.9 68.2 216.5 68.4 89.9 90.1 108.2
28 mC 249.2 68.2 216.5 68.4 90.1 90.1 71.8
39 mC 251.8 152.8 68.2 102.9 90.2 90.1 63.6
29 mC 251.8 68.2 152.8 102.9 90.1 90.2 63.6
41 mC 251.9 216.8 68.4 68.2 90.1 90.2 71.6
38 oC 252.4 68.2 152.8 102.9 89.9 90.2 116.4
40 oC 252.6 68.2 216.5 68.4 89.9 90.1 108.2
30 mC 252.9 68.2 216.5 68.4 90.1 90.1 71.8
12 hP 256.1 68.2 68.4 102.9 90.1 90.2 90.1

## Slide 39: Choose the lattice of highest symmetry and quality of fit<10
LATTICE- BRAVAIS- QUALITY UNIT CELL CONSTANTS (ANGSTROEM & DEGREES)
CHARACTER LATTICE OF FIT a b c alpha beta gamma
* 44 aP 0.0 68.2 68.4 102.9 90.1 90.2 90.1
* 31 aP 0.7 68.2 68.4 102.9 90.1 89.8 89.9
* 33 mP 1.4 68.2 68.4 102.9 90.1 90.2 90.1
* 34 mP 3.2 68.2 102.9 68.4 90.1 90.1 90.2
* 35 mP 3.3 68.4 68.2 102.9 90.2 90.1 90.1
* 32 oP 3.9 68.2 68.4 102.9 90.1 90.2 90.1
* 14 mC 5.5 96.5 96.7 102.9 89.9 90.2 89.8
* 10 mC 6.3 96.5 96.7 102.9 90.1 90.2 90.2
* 13 oC 6.9 96.5 96.7 102.9 89.9 90.2 89.8
* 11 tP 7.6 68.2 68.4 102.9 90.1 90.2 90.1
37 mC 248.2 216.5 68.2 68.4 90.1 90.1 71.8
36 oC 248.9 68.2 216.5 68.4 89.9 90.1 108.2
28 mC 249.2 68.2 216.5 68.4 90.1 90.1 71.8
39 mC 251.8 152.8 68.2 102.9 90.2 90.1 63.6
29 mC 251.8 68.2 152.8 102.9 90.1 90.2 63.6
41 mC 251.9 216.8 68.4 68.2 90.1 90.2 71.6
38 oC 252.4 68.2 152.8 102.9 89.9 90.2 116.4
40 oC 252.6 68.2 216.5 68.4 89.9 90.1 108.2
30 mC 252.9 68.2 216.5 68.4 90.1 90.1 71.8
12 hP 256.1 68.2 68.4 102.9 90.1 90.2 90.1
tP
tI
aP
mP
mC
oP
oC
oI
oF
hR
cP
cI
cF
hP

## Slide 40
LATTICE- BRAVAIS- QUALITY UNIT CELL CONSTANTS (ANGSTROEM & DEGREES)
CHARACTER LATTICE OF FIT a b c alpha beta gamma
* 44 aP 0.0 68.2 68.4 102.9 90.1 90.2 90.1
* 31 aP 0.7 68.2 68.4 102.9 90.1 89.8 89.9
* 33 mP 1.4 68.2 68.4 102.9 90.1 90.2 90.1
* 34 mP 3.2 68.2 102.9 68.4 90.1 90.1 90.2
* 35 mP 3.3 68.4 68.2 102.9 90.2 90.1 90.1
* 32 oP 3.9 68.2 68.4 102.9 90.1 90.2 90.1
* 14 mC 5.5 96.5 96.7 102.9 89.9 90.2 89.8
* 10 mC 6.3 96.5 96.7 102.9 90.1 90.2 90.2
* 13 oC 6.9 96.5 96.7 102.9 89.9 90.2 89.8
* 11 tP 7.6 68.2 68.4 102.9 90.1 90.2 90.1
37 mC 248.2 216.5 68.2 68.4 90.1 90.1 71.8
36 oC 248.9 68.2 216.5 68.4 89.9 90.1 108.2
28 mC 249.2 68.2 216.5 68.4 90.1 90.1 71.8
39 mC 251.8 152.8 68.2 102.9 90.2 90.1 63.6
29 mC 251.8 68.2 152.8 102.9 90.1 90.2 63.6
41 mC 251.9 216.8 68.4 68.2 90.1 90.2 71.6
38 oC 252.4 68.2 152.8 102.9 89.9 90.2 116.4
40 oC 252.6 68.2 216.5 68.4 89.9 90.1 108.2
30 mC 252.9 68.2 216.5 68.4 90.1 90.1 71.8
12 hP 256.1 68.2 68.4 102.9 90.1 90.2 90.1
tP
tI
***** INDEXING OF OBSERVED SPOTS IN SPACE GROUP # 1 *****
17548 OUT OF 25072 SPOTS INDEXED. (about 70%)

## Slide 41: Integration for image 004
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
1) Draw boundaries of each reflection
2) Sum the intensities recorded on each pixel within boundary.
3) Repeat for each spot on each image.

## Slide 42: Integration for first 10 images
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
1) Draw boundaries of each reflection
2) Sum the intensities recorded on each pixel within boundary.
3) Repeat for each spot on each image.

## Slide 43: Output integrated intensities
!UNIT_CELL_CONSTANTS= 67.918 67.918 102.177 90.000 90.000 90.000
! H, K, L, IOBS, SIGMA, XCAL, YCAL, ZCAL, RLP, PEAK,CORR,MAXC,XOBS, YOBS, ZOBS, ALF0,BET0,ALF1,BET1,PSI,ISEG
-47 -11 -7 2.545E+02 2.788E+02 2995.1 2344.0 604.8 1.38699 77.12746 4 33 2978.5 2336.6 605.0 45.91 0.07 -29.44 66.81 -118.54 1
-47 -11 -6 1.002E+03 3.147E+02 22.1 2318.8 94.9 1.39114 78.49145 10 32 29.5 2311.6 95.0 31.25 0.09 -151.27 66.62 95.30 1
-47 -11 -6 1.366E+02 2.771E+02 2994.8 2329.0 603.0 1.39049 79.95720 4 29 2987.3 2329.6 603.1 45.91 0.07 -29.01 66.72 -118.77 1
-47 -11 -5 1.872E+03 3.339E+02 21.5 2304.4 93.7 1.39492 92.47218 23 35 25.3 2304.5 93.7 31.25 0.09 -151.71 66.54 94.48 1
-47 -11 -5 1.204E+03 2.971E+02 2995.5 2314.6 601.1 1.39429 78.44115 15 30 2986.6 2311.4 601.0 45.91 0.07 -28.57 66.64 -118.99 1
-47 -11 -4 6.058E+02 3.242E+02 20.0 2290.6 92.4 1.39900 96.87422 12 77 27.5 2290.6 92.4 31.25 0.09 -152.15 66.47 93.68 1
-47 -11 -4 4.104E+02 2.919E+02 2992.3 2298.0 599.2 1.39845 80.31631 6 31 2982.4 2288.8 598.7 111.48 0.07 -28.13 66.51 -119.18 1
-47 -11 -3 2.735E+03 3.281E+02 17.5 2277.3 91.2 1.40337 95.48840 30 34 19.2 2279.0 91.4 31.25 0.09 -152.59 66.42 92.90 1
-47 -11 -3 9.144E+02 3.109E+02 2994.8 2284.8 597.4 1.40283 75.93009 17 32 2983.7 2282.7 597.4 111.48 0.07 -27.69 66.46 -119.37 1
-47 -11 -2 3.644E+02 2.749E+02 14.1 2264.4 89.9 1.40808 92.92796 6 35 19.6 2264.0 89.8 31.81 0.09 -153.04 66.39 92.13 1 -47 -11 .-47 -11 -1 1.441E+03 2.964E+02 9.7 2252.0 88.6 1.41308 87.63616 23 33 14.4 2252.3 88.7 32.14 0.09 -153.48 66.36 91.39 1
-47 -11 0 3.293E+02 2.450E+02 4.4 2240.0 87.3 1.41836 80.78474 7 31 12.0 2236.6 87.0 32.14 0.09 -153.93 66.36 90.67 1
-47 -10 -9 1.047E+03 3.427E+02 22.3 2316.5 100.7 1.39148 81.59772 16 32 23.3 2318.8 100.7 27.88 0.08 -151.33 66.60 97.62 1
-47 -10 -9 1.153E+02 2.993E+02 2994.5 2326.5 608.7 1.39095 80.67455 4 31 2987.2 2325.2 608.4 45.91 0.07 -28.94 66.70 -116.36 1
-47 -10 -8 4.724E+03 3.767E+02 25.0 2300.6 99.5 1.39410 96.97063 44 49 24.9 2301.0 99.2 31.13 0.08 -151.77 66.48 96.75 1
-47 -10 -8 2.220E+03 3.363E+02 2992.0 2310.8 606.8 1.39349 84.59594 24 33 2988.1 2309.9 606.5 45.91 0.07 -28.51 66.58 -116.63 1
-47 -10 -7 6.914E+03 3.802E+02 26.6 2285.5 98.3 1.39692 99.42799 57 56 29.5 2287.8 98.5 31.25 0.09 -152.20 66.37 95.90 1
-47 -10 -7 3.098E+03 3.250E+02 2990.5 2295.6 604.9 1.39632 86.71242 35 35 2985.3 2294.3 604.7 45.91 0.07 -28.08 66.47 -116.87 1
-47 -10 -6 1.589E+03 2.980E+02 27.3 2271.0 97.1 1.40004 99.54026 16 32 29.5 2272.9 97.1 31.25 0.09 -152.63 66.28 95.07 1
-47 -10 -6 9.778E+02 3.015E+02 2989.9 2281.0 603.0 1.39944 87.42934 11 33 2984.9 2278.8 602.7 45.91 0.07 -27.65 66.38 -117.11 1
-47 -10 -5 1.086E+03 3.186E+02 27.1 2257.0 95.8 1.40345 99.49097 13 33 23.1 2258.3 95.7 31.25 0.09 -153.06 66.20 94.25 1
-47 -10 -5 7.046E+02 3.209E+02 2990.2 2267.0 601.2 1.40285 86.86985 8 33 2986.2 2270.9 601.7 45.91 0.07 -27.22 66.30 -117.33 1
-47 -10 -4 5.056E+03 3.658E+02 25.9 2243.5 94.6 1.40716 99.29475 48 45 27.0 2247.1 94.5 31.25 0.09 -153.50 66.14 93.46 1
-47 -10 -4 2.003E+03 3.387E+02 2986.7 2250.9 599.3 1.40664 89.14124 26 34 2985.0 2252.7 599.2 111.36 0.07 -26.79 66.17 -117.53 1
-47 -10 -3 8.050E+02 3.299E+02 23.8 2230.4 93.3 1.41117 98.79202 16 44 24.0 2225.9 92.9 31.25 0.09 -153.93 66.09 92.69 1
-47 -10 -3 7.560E+02 3.407E+02 2988.8 2237.9 597.5 1.41066 86.07878 7 31 2984.3 2240.7 597.5 111.48 0.07 -26.35 66.12 -117.73 1
-47 -10 -2 3.435E+03 3.298E+02 20.8 2217.9 92.0 1.41550 97.47218 30 44 23.3 2220.1 92.1 31.25 0.09 -154.37 66.05 91.93 1
-47 -10 -2 1.502E+03 3.296E+02 2991.9 2225.3 595.7 1.41499 81.04167 19 38 2987.7 2223.9 595.6 111.48 0.07 -25.91 66.08 -117.92 1
-47 -10 -1 1.185E+03 3.234E+02 16.8 2205.7 90.7 1.42013 94.89558 14 34 23.3 2203.6 91.0 31.25 0.09 -154.81 66.03 91.20 1
-47 -10 0 4.880E+02 3.137E+02 11.8 2193.8 89.4 1.42512 90.43126 12 35 17.5 2193.4 89.6 32.13 0.09 -155.26 66.02 90.47 1
-47 -10 1 7.198E+02 2.775E+02 6.1 2182.4 88.1 1.43037 82.80218 15 34 14.4 2180.9 88.0 32.14 0.09 -155.70 66.03 89.77 1
-47 -9 -11 1.625E+04 5.170E+02 16.5 2302.1 105.2 1.39783 89.53320 83 75 18.8 2303.5 105.5 27.87 0.08 -151.85 66.58 99.11 1
-47 -9 -10 3.139E+03 3.181E+02 21.4 2285.6 104.0 1.39940 97.73439 28 45 23.9 2286.7 104.1 27.87 0.08 -152.27 66.43 98.22 1
-47 -9 -10 1.502E+03 2.902E+02 2994.5 2294.9 610.6 1.39895 79.06115 25 34 2985.4 2292.3 610.5 56.07 0.07 -27.99 66.52 -114.47 1
-47 -9 -9 1.269E+03 3.169E+02 25.2 2269.7 102.8 1.40127 99.12431 15 33 24.9 2272.3 102.7 27.87 0.08 -152.69 66.30 97.34 1
-47 -9 -9 3.660E+02 3.163E+02 2991.9 2279.6 608.7 1.40076 84.73209 6 31 2980.7 2278.0 608.8 45.91 0.07 -27.58 66.40 -114.75 1
-47 -9 -8 3.405E+02 2.993E+02 28.1 2254.4 101.6 1.40342 99.61732 5 36 33.8 2251.4 101.8 27.87 0.08 -153.12 66.17 96.49 1
-47 -9 -8 5.246E+02 3.242E+02 2989.1 2264.3 606.9 1.40292 88.66219 7 31 2979.4 2256.8 606.8 45.91 0.07 -27.15 66.27 -115.01 1
INTEGRATE.HKL file has 1,238,805 lines from this 1.4 Å data set ProK

## Slide 44: Intensity weighted reciprocal lattice, sectioned along c*, cutoff at 8 Å resolution for clarity
L=-12
L=-11
L=-10
L=-9
L=-8
L=-7
L=-6
L=-5
L=-4
L=-3
L=-2
L=-1
L=-0
L=+1
L=+2
L=+3
L=+4
L=+5
L=+6
L=+7
L=+8
L=+9
L=+10
L=+11
L=+12

## Slide 45: Intensity weighted reciprocal lattice, sectioned along c*, cutoff at 8 Å resolution for clarity
L=+12
L=+11
L=+10
L=+9
L=+8
L=+7
L=+6
L=+5
L=+4
L=+3
L=+2
L=+1
L=-0
L=-1
L=-2
L=-3
L=-4
L=-5
L=-6
L=-7
L=-8
L=-9
L=-10
L=-11
L=-12

## Slide 46: Primitive Tetragonal lattices allow point group symmetries 4 or 422. Which fits our diffraction pattern?
System | Bravais lattice | Point group | 65 Chiral Space Groups |  |  |  |  | 
Triclinic | P | 1 | P1 |  |  |  |  | 
Monoclinic | P | 2 | P2 | P21 |  |  |  | 
 | C |  | C2 |  |  |  |  | 
Orthorhombic | P | 222 | P222 | P2221 | P21212 | P212121 |  | 
 | C |  | C2221 | C222 |  |  |  | 
 | F |  | F222 |  |  |  |  | 
 | I |  | I222 | I212121 |  |  |  | 
Tetragonal | P | 4 | P4 | P41 | P42 | P43 |  | 
 | I |  | I4 | I41 |  |  |  | 
 | P | 422 | P422 | P4212 | P4122 | P41212 | P4222 | P42212
 |  |  | P4322 | P43212 |  |  |  | 
 | I |  | I422 | I4122 |  |  |  | 
Trigonal/ Rhombo-hedral | P | 3 | P3 | P31 | P32 |  |  | 
 | R |  | R3 |  |  |  |  | 
 | P | 32 | P312 | P321 | P3112 | P3121 | P3212 | P3221
 | R |  | R32 |  |  |  |  | 
Hexagonal | P | 6 | P6 | P61 | P62 | P63 | P64 | P65
 |  | 622 | P622 | P6122 | P6222 | P6322 | P6422 | P6522
Cubic | P | 23 | P23 | P213 |  |  |  | 
 | F |  | F23 |  |  |  |  | 
 | I |  | I23 | I213 |  |  |  | 
 | P | 432 | P432 | P4232 | P4332 | P4132 |  | 
 | F |  | F432 | F4132 |  |  |  | 
 | I |  | I432 | I4132 |  |  |  | 
4
422

## Slide 47
Point group 4
Point group 422
P4
H, K,L
-H,-K,L
-K, H,L
K,-H,L
-H, K,-L
H,-K,-L
K, H,-L
-K,-H,-L
P422
4-fold symmetry &
perpendicular 2-folds
4-fold symmetry

## Slide 48: What rotational symmetry do you see?
90° rotational symmetry

## Slide 49: 2-fold rotation on vertical axis
This rotation axis coincides with a mirror plane.

## Slide 50: 2-fold axis in the plane appears as a mirror
Mirror-related spots are equidistant from vertical mirror plane

## Slide 51: 2-fold axis in the plane appears as mirror
Mirror-related spots are equidistant from horizontal mirror plane

## Slide 52: How many symmetry copies of this reflection do you see?
What are their indices?
3,8,0

## Slide 53: 8 symmetry equivalents
a*
b*
What are the symmetry operators that relate these reflections?
3,8,0
Notes: Here it is easy to guess the symmetry operations. We see the integers 3 and 8 appearing in all the symmetry equivalent h,k,l values, but they differ in +/- sign, and sometimes 3 and 8 swap positions. (i.e. sometimes 3 is the h value, sometimes 3 is the k value. In this case, we get the symmetry operators by replacing all instances of 3 with “h” and all instances of 8 with “k”.

## Slide 54: 8 symmetry equivalents
a*
b*
3,8,0
8,3,0
8,-3,0
3,-8,0
-3,-8,0
-8,-3,0
-8, 3,0
-3,8,0
What are the symmetry operators that relate these reflections?
Notes: Here it is easy to guess the symmetry operations. We see the integers 3 and 8 appearing in all the symmetry equivalent h,k,l values, but they differ in +/- sign, and sometimes 3 and 8 swap positions. (i.e. sometimes 3 is the h value, sometimes 3 is the k value. In this case, we get the symmetry operators by replacing all instances of 3 with “h” and all instances of 8 with “k”.

## Slide 55: Symmetry operators in reciprocal space
-3,-8,0
a*
b*
3,8,0
8,3,0
8,-3,0
3,-8,0
-8,-3,0
-8, 3,0
-3,8,0
-k,-h,0
-k, h,0
h,k,0
-h,-k,0
-h,k,0
k,h,0
k,-h,0
h,-k,0
422
h, k,0
-h, k,0
h,-k,0
-h,-k,0
k, h,0
-k, h,0
k,-h,0
-k,-h,0
Notes: Here it is easy to guess the symmetry operations. We see the integers 3 and 8 appearing in all the symmetry equivalent h,k,l values, but they differ in +/- sign, and sometimes 3 and 8 swap positions. (i.e. sometimes 3 is the h value, sometimes 3 is the k value. In this case, we get the symmetry operators by replacing all instances of 3 with “h” and all instances of 8 with “k”.

## Slide 56: Benefit of determining the point group symmetry of our data set.
Accuracy of intensity values will improve if we average together the values of symmetry-related reflections (i.e. merging).
But, we must discern the correct rotational symmetry laws that relate lattice points (point group symmetry. It would be convenient to quantify how well the pattern obeys a certain point group symmetryRmerge.

## Slide 57
j observations of the reflection 30 22 6
<I>= (550 + 500 + 543) / 3
= 531
j | H | K | L | I
1 | 30 | 22 | 6 | 550
2 | -30 | -22 | 6 | 500
3 | 30 | -22 | -6 | 543
Rmerge= S|Ij-<I>|
SIj
Discrepancy
between symmetry related reflections
S|Ij-<I>| = |550-531|+|500-531|+|543-531|
= 19 + 31 + 12
= 62
SIj = 550 + 500 + 543
= 1593
Rmerge = 62/1593 = 0.039 = 3.9%
?
H, K, L=
-H,-K, L=
H,-K,-L

## Slide 58: What Rmerge is expected for these 2 data sets if we assume P4 symmetry?
Point group 4
Point group 422
Rmerge P4 <20%
Rmerge P4<20%

## Slide 59: What Rmerge is expected for these 2 data sets if we assume 422 symmetry?
Point group 4
Point group 422
Rmerge P422 >50%
Rmerge P422<20%

## Slide 60: Merge symmetry-related measurements
Average together intensity values of reflections related by these reciprocal space symmetry operators.
Plane L=0
b*
a*
true?
H, K, L=
-K, H, L=
-H, K, L=
K,-H, L=
K, H,-L=
-H, K,-L=
-K,-H,-L=
H,-K,-L=
Plane L=0
b*
a*
K, H,-L
H,K,L
H,-K, -L
K, -H,L
-K,H,L
-H,-K,L
-H, K,-L
-K,-H,-L
Asymmetric unit of reciprocal space.

## Slide 61
Discrepancy between symmetry related reflections (Rmerge or Rsym) increases with higher resolution. Why?
Shell | Rmerge
100-5.0Å | 0.04
5.0-3.0Å | 0.06
3.0-2.0Å | 0.08
2.0-1.7Å | 0.15
Overall | 0.07
Statistics are analyzed as a function of resolution (N shells).

## Slide 62
Average I/s decreases with increasing resolution
Conservatives would say high resolution shells with I/s <2 should be discarded.
Shell | I/sI
100-5.0 Å | 20.0
5.0-3.0 Å | 10.0
3.0-2.0 Å | 7.0
2.0-1.7 Å | 3.0
Overall | 8.2
SIGNAL TO NOISE RATIO (I/s)

## Slide 63
CC½ measures the correlation between symmetry-related halves of the unmerged data set.
Shell | CC ½
100-5.0 Å | 0.99
5.0-3.0 Å | 0.99
3.0-2.0 Å | 0.97
2.0-1.7 Å | 0.55
Overall | 0.98
Correlation Coefficient (CC½)
CC½ decreases with increasing resolution.
Diederichs & Karplus say resolution shells with CC ½ > 0.30 have usable information content.

## Slide 64
COMPLETENESS?
What percentage of reciprocal
Lattice was measured for a given
Resolution limit?
Better than 90% I hope.
Shell | completeness
100-5.0Å | 99.9%
5.0-3.0Å | 95.5%
3.0-2.0Å | 89.0%
2.0-1.7Å | 85.3%
Overall | 92.5%
Missing wedges of data.

## Slide 65: Assignment

## Slide 66: The End

## Slide 67: Each circle corresponds to a different reciprocal lattice plane
Start indexing process using reflections within the same plane and lying near the origin.

## Slide 68: What are some reasons why indexing might be inaccurate or unreliable?
The wavelength of the incident radiation
Coordinates (X,Y) of the direct beam
Coordinates (X,Y) for the spot position
Unit cell parameters
a,b,c, a,b,g
The orientation of the unit cell axes with respect to the laboratory axes (fyk).

## Slide 69: Determine unit cell length “b” Standard detector geometry
X-ray beam
0,-1 reflection
1,0,0
(0,0,0)
origin of reciprocal lattice,
Also known as
x-beam, y-beam
crystal
DCF=80 mm
Db*=2.0 mm
b*
FILM
1/l
2d•sinq = nl
2b•sinq = l
b = l/(2•sinq)
q
q
tan2q = Db/DCF
q = ½•arctan(Db/DCF)
b = l/(2•sin(½•arctan(Db/DCF))
b = 1.54Å /(2•sin(½•arctan(2.0mm/80mm))
b = 61.6 Å
b

## Slide 70: Systematic Absences
To reveal the pattern of systematic absences to students in our data processing labs this week, I wrote a script called "absences.com" . (/joule2/programs/lx_bin/absences.com)
Just type "absences.com" followed by the name of the scalepack file, like this:
absences.com prok_pcmbs_jonathan_screen.sca
And the script will display the intensities and I/sigmas for axial reflections. The pattern of absences becomes very clear. For this to work, we must process the data in P422 (not P43212), so both strong and weak reflections are reported:
SAYRE:process_denzo[267] absences.com prok_pcmbs_jonathan_screen.sca
Data_set = prok_pcmbs_jonathan_screen.sca
=============== h 0 0 reflections ==============
h k l I sigma I/sigma
1, 0, 0, -1.6, 0.3, -5.3
3, 0, 0, 67.7, 7.6, 8.9
4, 0, 0, 40995.8, 601.8, 68.1
5, 0, 0, 3.0, 11.8, 0.3
6, 0, 0, 10600.2, 160.8, 65.9
7, 0, 0, 3.3, 16.1, 0.2
8, 0, 0, 3918.5, 65.0, 60.3
9, 0, 0, 17.2, 18.3, 0.9
10, 0, 0, 10876.2, 170.6, 63.8
11, 0, 0, 19.5, 20.0, 1.0
12, 0, 0, 121996.0, 1913.0, 63.8
13, 0, 0, 17.2, 25.3, 0.7
14, 0, 0, 116394.0, 1708.0, 68.1
15, 0, 0, -22.3, 26.2, -0.9
16, 0, 0, 16599.7, 259.0, 64.1
17, 0, 0, -75.9, 34.3, -2.2
18, 0, 0, 108.0, 33.6, 3.2
19, 0, 0, 30.7, 31.0, 1.0
20, 0, 0, 2312.2, 59.0, 39.2
21, 0, 0, -55.6, 37.6, -1.5
22, 0, 0, 767.9, 44.4, 17.3
23, 0, 0, -59.1, 32.5, -1.8
24, 0, 0, 44461.4, 869.0, 51.2
25, 0, 0, 105.9, 38.5, 2.8
26, 0, 0, 1704.0, 68.0, 25.1
27, 0, 0, -11.4, 32.1, -0.4
28, 0, 0, 3235.7, 92.9, 34.8
29, 0, 0, 6.3, 45.5, 0.1
30, 0, 0, 4327.6, 151.7, 28.5
31, 0, 0, -54.7, 39.3, -1.4
32, 0, 0, 1293.9, 52.7, 24.6
33, 0, 0, 36.4, 44.3, 0.8
34, 0, 0, 3211.6, 124.8, 25.7
35, 0, 0, -57.0, 39.2, -1.5
36, 0, 0, 15.1, 38.0, 0.4
37, 0, 0, 8.2, 33.7, 0.2
38, 0, 0, -39.2, 35.6, -1.1
39, 0, 0, 59.1, 38.8, 1.5
40, 0, 0, 2202.7, 68.2, 32.3
41, 0, 0, -5.4, 35.4, -0.2
42, 0, 0, 2128.8, 67.0, 31.8
43, 0, 0, 16.1, 31.0, 0.5
44, 0, 0, 1088.4, 47.0, 23.2
45, 0, 0, 32.0, 29.9, 1.1
46, 0, 0, 341.3, 34.6, 9.9
47, 0, 0, -38.6, 31.0, -1.2
48, 0, 0, 387.8, 60.4, 6.4
============== 0 k 0 reflections ==============
h k l I sigma I/sigma
============== 0 0 l reflections ==============
h k l I sigma I/sigma
0, 0, 2, -8.6, 1.8, -4.8
0, 0, 3, 12.1, 12.8, 0.9
0, 0, 5, 19.4, 12.1, 1.6
0, 0, 6, 43.8, 18.6, 2.4
0, 0, 7, 19.5, 15.5, 1.3
0, 0, 8, 23681.6, 497.1, 47.6
0, 0, 9, 22.1, 21.3, 1.0
0, 0, 10, 66.2, 33.8, 2.0

## Slide 73: Diffracted intensities arise as if reflecting from families of planes --William Bragg.
(0,1) planes
a
b
Crystal
(1,1) planes
(2,1) planes
(3,1) planes
(0,2) planes
(1,2) planes
(2,2) planes
(3,2) planes
Xrays
Detector

## Slide 74: What are the chances of observing reflections from all these planes in a single orientation?
(0,1) planes
Crystal
(1,1) planes
(2,1) planes
(3,1) planes
(0,2) planes
(1,2) planes
(2,2) planes
(3,2) planes
a
b
Xrays
Detector
Excellent
Zero

## Slide 75: The planes must be oriented w.r.t the X-ray beam such that the difference in path length of each scattered ray is nl.
Crystal
(1,1) planes
a
b
Xrays
Detector
Difference in path lengths is not nl.
Scattered waves are out of phase.
Total destructive interference.
(1,1) reflection not observed in this crystal orientation.
2dsinq

## Slide 76: Sphere of reflection shows the relationship between Bragg plane (HKL) and location of reflection (HKL) on detector
Reciprocal Lattice
a*
b*
a
b
Crystal
Xrays
Detector
1/l

## Slide 77: (0,1) Bragg planes produce (0,1) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(0,1) planes
length=1/d0,1
(0,1)
a
b
Crystal
Detector
Xrays

## Slide 78: (1,1) Bragg planes produce (1,1) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(1,1) planes
length=1/d1,1
(1,1)
a
b
(0,1)
Crystal
Detector
Xrays

## Slide 79: (2,1) Bragg planes produce (2,1) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(2,1) planes
length=1/d2,1
(1,1)
(0,1)
a
b
(2,1)
Crystal
Detector
Xrays

## Slide 80: (3,1) Bragg planes produce (3,1) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(3,1) planes
length=1/d3,1
(1,1)
(0,1)
a
b
(2,1)
(3,1)
Crystal
Detector
Xrays

## Slide 81: (0,2) Bragg planes produce (0,2) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(0,2) planes
length=1/d0,2
(1,1)
(0,1)
(2,1)
(3,1)
(0,2)
a
b
Crystal
Detector
Xrays

## Slide 82: (1,2) Bragg planes produce (1,2) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(1,2) planes
length=1/d1,2
(1,1)
(0,1)
(2,1)
(3,1)
(0,2)
(1,2)
a
b
Crystal
Detector
Xrays

## Slide 83: (2,2) Bragg planes produce (2,2) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(2,2) planes
length=1/d2,2
(1,1)
(0,1)
(2,1)
(3,1)
(2,2)
(0,2)
(1,2)
a
b
Crystal
Detector
Xrays

## Slide 84: (3,2) Bragg planes produce (3,2) reciprocal lattice point
RECIPROCAL LATTICE
a*
b*
(3,2) planes
length=1/d3,2
(1,1)
(0,1)
(2,1)
(3,1)
(2,2)
(0,2)
(1,2)
(3,2)
a
b
Crystal
Detector
Xrays

## Slide 85: And so on... to fill out reciprocal lattice.
RECIPROCAL LATTICE
a*
b*
(1,1)
(0,1)
(2,1)
(3,1)
(2,2)
(0,2)
(1,2)
(3,2)
a
b
Crystal
Detector
Xrays
(1,0)
(2,0)
(3,0)
(1,-2)
(2,-2)
(3,-2)
(2,-1)
(1,-1)
(3,-1)
(0,-1)
(0,-2)
(-1,1)
(-1,2)
(-1,0)
(-1,-2)
(-1,-1)
(-2,1)
(-2,2)
(-2,0)
(-2,-2)
(-2,-1)
(-3,1)
(-3,2)
(-3,0)
(-3,-2)
(-3,-1)
In this crystal orientation Which reflections will appear on the detector?

## Slide 86: What operation must we perform to the crystal in order to observe the (1,1) reflection?
RECIPROCAL LATTICE
a*
b*
(1,1) planes
(1,1)
a
b
Crystal
Detector
Xrays
33°

## Slide 87: Rotate crystal to observe (1,1) reflection.
RECIPROCAL LATTICE
(1,1) planes
a*
b*
(1,1)
Crystal
Detector
Xrays
a
b
(1,1) reflection is located here!

## Slide 88: A crystal rotation that brings the reciprocal lattice point (HKL) in contact with sphere of reflection, satisfies Bragg’s Law for reflection (HKL).
a
b
a
b
(1,1) planes
(1,1)
Crystal
Detector
Xrays
q
1/l
d*
d*/2 = 1/l•sinq
2d•sinq = l
}
(1,1) reflection is located here!
RECIPROCAL LATTICE

## Slide 89: Indexing - We observe the location of a reflection on the detector. Which set of Bragg planes produced it?
a
b
a
b
(1,1) planes
(1,1)
Crystal
Detector
Xrays
There is a reflection located here!
What is it’s index?
RECIPROCAL LATTICE
a*
b*
How many increments of a* and b* is this point from the origin?
d*=ha*+ kb*+ lc*

## Slide 90: We collected a series of images, each covering 1° rotation. Here we rotate 15° per image.
1/l
RECIPROCAL PLANE
Crystal
Detector
Xrays
5°
DCF
X,Y

## Slide 91: We collected a series of exposure while crystal rotates.
RECIPROCAL PLANE
Crystal
Detector
Xrays
13°

## Slide 92: We collected a series of exposure while crystal rotates.
RECIPROCAL PLANE
Crystal
Detector
Xrays
15°

## Slide 93: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°

## Slide 94: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°

## Slide 95: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°

## Slide 96: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°
45-60°

## Slide 97: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°
45-60°
60-75°

## Slide 98: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°
45-60°
60-75°
75-90°

## Slide 99: Map onto reciprocal lattice
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°
45-60°
60-75°
75-90°
90-105°

## Slide 100: Map onto reciprocal lattice
a*
b*
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°
45-60°
60-75°
75-90°
a
b

## Slide 101: Map onto reciprocal lattice
a*
b*
RECIPROCAL LATTICE
Crystal
Xrays
Image rotation
0-15°
15-30°
30-45°
45-60°
60-75°
75-90°
(1,-2)
(2,-2)
(3,-2)
(0,-2)
(-1,-2)
(-2,-2)
(-3,-2)
(2,-1)
(1,-1)
(3,-1)
(0,-1)
(-1,-1)
(-2,-1)
(-3,-1)
(1,0)
(2,0)
(3,0)
(-1,0)
(-2,0)
(-3,0)
(1,1)
(0,1)
(2,1)
(3,1)
(-1,1)
(-2,1)
(-3,1)
(2,2)
(0,2)
(1,2)
(3,2)
(-1,2)
(-2,2)
(-3,2)
a
b

## Slide 102: Map onto reciprocal lattice
a*
b*
RECIPROCAL LATTICE
Crystal
Xrays
a
b

## Slide 103: Wave 1 travels 2dsinq=l farther than wave 2 and interferes constructively with it because it is in phase In general: 2dhklsinqhkl=nl
l
wave 2
wave 1
d sin q
q
q
d
atomic
plane
atomic
plane
reflected angle
incident angle
q
q
n=1
d
l

## Slide 104: Reflections are observable from a set of Bragg planes only when radiation paths differ by integer multiples of λ. 2dhklsinqhkl=nl = Bragg’s Law
a
b
reflection
Crystal
Detector
(0,1) Bragg Planes
X-ray
Source

## Slide 105: Determine unit cell length “b” Precession camera geometry (undistorted)
Db*=1.99 mm
FILM
X-ray beam
(0,-1,0) reflection
1,0,0
(0,0,0)
origin of reciprocal lattice,
Also known as
x-beam, y-beam
crystal
DCF=80 mm
b*
1/l
2d•sinq = nl
2b•sinq = l
b = l/(2•sinq)
q
q
b*/1/ l = Db/DCF
b* = Db/DCF•1/ l
b = l • DCF / Db
b = 1.54Å • 80mm/1.99mm
b = 61.6 Å
b