## Slide 1: Data Reduction Goals
From a series of diffraction images, measure reflection intensities (Ihkl) and standard deviation (shkl) for each reflection, hkl. Store the values in a file.
H K L I s
0 0 4 3295.4 174.0
0 0 8 482.1 28.7
0 0 12 9691.0 500.7
0 0 16 1743.9 67.4
0 0 20 5856.0 221.0
0 0 24 14066.5 436.2
0 0 28 9936.3 311.7
0 0 36 8409.8 273.4
0 0 40 790.5 32.8
0 0 44 103.4 18.4
. . . . .
. . . . .
. . . . .
37 7 0 28.5 16.2
37 7 1 110.1 10.9
37 7 2 337.4 13.3
37 7 3 98.5 10.6
37 7 4 25.9 10.7
Set of 720 images.
Each image covers 0.5°
Final intensities
Index
Integrate
Merge
13,000 Mb
2 Mb
720
719
718
717
716

## Slide 2: Along the way, we will determine the crystal’s unit cell parameters & space group
Before we even put the crystal in the beam, we can rule out 165 choices as being incompatible with the chirality of Proteinase K.
There are 230 space groups possible.
  Hence, the appearance of “230” in our course name “Chem230A.”
We can rule out the165 space groups that contain mirror symmetry because mirrors are incompatible with natural proteins like ProK.
  In order for a crystal to have mirror symmetry, left AND right handed versions of the molecule must be present.
  Proteinase K is produced using only L-amino acids (left).
  Therefore, our sample of ProK could not crystallize in a space group with mirror symmetry
ProK can crystallize only in one of the 65 space groups that lack mirrors, (i.e. chiral space groups, or Sohncke space groups).
Mirror plane
left
right
Unit cell of a crystal with Pm symmetry requires left & right hands.

## Slide 3: Identify Bravais lattice type by recognizing the spatial arrangement of reflections in 3D.
Crystal space
Diffraction space
Square
unit cell
Oblique
unit cell
Square
reciprocal lattice
Oblique
reciprocal lattice

## Slide 4: Identify Point group symmetry by recognizing the pattern of diffraction intensities.
Crystal space
Diffraction space
4-fold symmetry
in motif
4-fold symmetry
In intensity pattern
2-fold symmetry
in motif
2-fold symmetry
In intensity pattern

## Slide 5: Summary: Space group determination is a stepwise process of elimination.
System | Bravais lattice | Point group | 65 Chiral Space Groups |  |  |  |  | 
Triclinic | P | 1 | P1 |  |  |  |  | 
Monoclinic | P | 2 | P2 | P21 |  |  |  | 
 | C |  | C2 |  |  |  |  | 
Orthorhombic | P | 222 | P222 | P2221 | P21212 | P212121 |  | 
 | C |  | C2221 | C222 |  |  |  | 
 | F |  | F222 |  |  |  |  | 
 | I |  | I222 | I212121 |  |  |  | 
Tetragonal | P | 4 | P4 | P41 | P42 | P43 |  | 
 | I |  | I4 | I41 |  |  |  | 
 | P | 422 | P422 | P4212 | P4122 | P41212 | P4222 | P42212
 |  |  |  |  | P4322 | P43212 |  | 
 | I |  | I422 | I4122 |  |  |  | 
Trigonal/ Rhombo-hedral | P | 3 | P3 | P31 | P32 |  |  | 
 | R |  | R3 |  |  |  |  | 
 | P | 32 | P312 | P321 | P3112 | P3121 | P3212 | P3221
 | R |  | R32 |  |  |  |  | 
Hexagonal | P | 6 | P6 | P61 | P62 | P63 | P64 | P65
 |  | 622 | P622 | P6122 | P6222 | P6322 | P6422 | P6522
Cubic | P | 23 | P23 | P213 |  |  |  | 
 | F |  | F23 |  |  |  |  | 
 | I |  | I23 | I213 |  |  |  | 
 | P | 432 | P432 | P4232 | P4332 | P4132 |  | 
 | F |  | F432 | F4132 |  |  |  | 
 | I |  | I432 | I4132 |  |  |  | 
Eliminate 165 achiral space groups. Choose among 65 chiral space groups. These 65 are compatible with L-protein.
Identify Bravais lattice: examine geometrical arrangement of reflections (e.g. primitive tetragonal).
Identify point group symmetry of reflection intensities: examine the rotational symmetry in the pattern of reflection intensities (e.g. 4 vs 422).
Distinguish between rotation or screw axis symmetry: examine systematic absences in reflection intensities (e.g. P422 vs. P41212
Distinguish handedness, if option exists (e.g. P41212 vs P43212)
1
2
3
4
5

## Slide 6: Review Data Collection
Let’s review the geometry of data collection so that we can understand how to index reflections.
Watch this simulated data collection video:
  Collect 90° of data in 18 images (5° wedges)
  XrayView software.

## Slide 7
Crystal
X-ray beam
Reciprocal
lattice
Ewald’s sphere of reflection
Detector
Diffracted rays
Simulated Data Collection

## Slide 8: Indexing an oscillation image appear challenging
The reciprocal lattice is only partly represented. You see only those reflections that obey Bragg’s Law during a small rotation.
The reciprocal lattice is distorted. You see a 2D projections of a 3D lattice—a dimension of depth is lost.
Orientation of reciprocal cell vectors a*, b*, c* are not necessarily aligned with film edges— the orientation of the crystal in the loop is arbitrary.
The concept of Ewald’s sphere will help us.
Oscillation image.

## Slide 9: For a given spot on the film, we need to trace the diffracted ray back to the reciprocal lattice point (h,k,l)
What’s the h,k,l of this spot?
3 lattice points in a* direction
2 lattice points in b* direction
The answer is HKL=3,2,2
What parameters must be
defined to complete this construction?

## Slide 10: You can Index by Inspection from a precession photo
Recall that spots are arrayed on a reciprocal lattice.
Count how many steps the given reflection is displaced from the origin.
  h=Number of steps of a*.
  k=Number of steps of b*.
  l=Number of steps of c*.
Buerger Precession Camera
Precession Photograph

## Slide 11: Index the reflection circled in cyan.
What pieces of information are required to index this reflection?
1) Define lattice points
2) Define a*,b*, c* direction & length
3) Locate origin.

## Slide 12: Mark lattice points with red circles.
Note the spacing between reflections is periodic.
Draw evenly spaced lines through the spots to define the spacings a* & b*

## Slide 13: Draw evenly spaced lines thru spots
A wider reciprocal spacing gives smaller (better) real cell spacing.
Draw another set of evenly spaced lines at 90° or 120°, if possible.

## Slide 14: 90˚ is most simplifying choice

## Slide 15: Weak reflections not detected previously can be predicted at lattice points. Note: we didn’t need to identify the position of every spot to get the lattice.

## Slide 16: Locate origin of reciprocal lattice
Origin is located where direct x-ray beam intercepts image. To see it, briefly remove beam-stop.

## Slide 17: Origin is defined. Now, label a* & b*
a*
b*
What is the index of the spot?
a*
b*

## Slide 18: Reflection h,k,l is 3,8,0
a*
b*
a*
a*
a*
b*
b*
b*
b*
b*
b*
b*
b*
3rd column on the right side of the origin.
8th row above the origin

## Slide 19: Which Bravais Lattice fits this pattern?
a*
b*
a*
b*
a* and b* have the same length.
They are perpendicular to each other.

## Slide 20: Which Bravais Lattice fits this pattern?
a=b and g=90°

## Slide 21: Next, index spots on an oscillation image.
This is easy!
But, what about this?
Confusing! 3D reciprocal lattice projected on 2D detector.

## Slide 22: Use Ewald Sphere construction to map 2D spots back to 3D reciprocal lattice.
detector
In an undistorted view of the reciprocal lattice, recorded reflections would reside on the surface of a sphere, not a plane.
a*
c*
b*

## Slide 23: A distortion-corrected representation of the reflections a single image reveals all 6 unit cell parameters

## Slide 24: Restored depth of the diffraction pattern is evident from an orthogonal view

## Slide 25: The automatic indexing algorithm in XDS can automatically identify spot positions, interpret crystal orientation, and unit cell dimensions.
Kabsch, W. (1988a) Automatic Indexing of Rotation Diffraction Patterns. J. Appl. Cryst. 21, 67–72.

## Slide 26: Locate spot positions with COLSPOT
!====================== JOB CONTROL PARAMETERS ===============================
JOB= ALL !XYCORR INIT COLSPOT IDXREF DEFPIX XPLAN INTEGRATE CORRECT
!====================== GEOMETRICAL PARAMETERS ===============================
ORGX=1506.23 ORGY=1503.91 !Detector origin (pixels). Calibrated by DC 03/01/2019
DETECTOR_DISTANCE=-74 !(mm)
ROTATION_AXIS= 0.0 1.0 0.0
OSCILLATION_RANGE=0.5 !degrees (>0)
X-RAY_WAVELENGTH=1.5418 !Angstrom
INCLUDE_RESOLUTION_RANGE=100.0 1.4
!==================== SELECTION OF DATA IMAGES ==============================
NAME_TEMPLATE_OF_DATA_FRAMES=i/prok_pcmbs_esmeralda????.osc DIRECT RAXIS
DATA_RANGE= 1 720 !First and last diffraction images collected
BACKGROUND_RANGE=1 4 !First and last data image for background
SPOT_RANGE= 1 10 !First and last data image number for finding spots
SPOT_RANGE= 171 180 !First and last data image number for finding spots
!============================================================================
XDS.INP file specifies automatic indexing instructions

## Slide 27
001 002 003 004 005
006 007 008 009 010
171 172 173 174 175
176 177 178 179 180

## Slide 28
001 002 003 004 005
006 007 008 009 010
171 172 173 174 175
176 177 178 179 180

## Slide 29
001 002 003 004 005
006 007 008 009 010
171 172 173 174 175
176 177 178 179 180

## Slide 30: SPOT.XDS
Spot position intens-
X Y phi ity
1504.01 1378.41 173.66 4537.
1526.45 1409.21 172.51 4485.
1499.41 1575.97 3.49 4395.
1499.77 1247.89 175.02 4004.
1482.28 1251.21 175.64 3430.
1460.42 1235.69 178.37 3111.
1515.65 1235.92 4.29 2099.
1516.82 1246.26 175.68 2043.
1494.83 1721.10 5.95 2002.
1460.63 1751.46 173.68 1935.
1496.21 1889.74 173.68 1869.
1536.70 1371.16 178.43 1775.
1509.20 1578.62 5.50 1705.
1520.18 1374.85 177.59 1695.
1480.15 1261.73 3.54 1664.
1471.50 1863.84 7.45 1649.
1470.76 1382.48 171.31 1644.
1500.62 1680.58 6.31 1643.
1563.73 1808.92 2.41 1613.
1460.22 1420.42 171.54 1604.
1472.21 1173.36 7.24 1589.
1510.04 1148.16 5.10 1539.
1448.42 1257.31 173.54 1534.
1511.90 1318.37 173.95 1452.
1560.73 1612.72 178.46 1448.
1532.31 1222.84 173.71 1417.
1491.13 1159.51 6.08 1363.
1551.09 1095.47 176.33 1360.
1574.56 1223.31 1.50 1278.
1510.01 1802.89 5.71 1266.
1548.82 1523.06 5.03 1213.
1426.96 1242.19 174.81 1210.
NUMBER OF DIFFRACTION SPOTS LOCATED 25118
IGNORED BECAUSE OF SPOT CLOSE TO UNTRUSTED REGION 13
WEAK SPOTS OMITTED 22
NUMBER OF DIFFRACTION SPOTS ACCEPTED 25083

## Slide 31: Draw vectors between reciprocal lattice points. For simplicity, only points from image 8 are shown.

## Slide 32: Vectors of same length & direction are grouped together
65 vectors like this:

## Slide 33: Vectors of same length & direction are grouped together
53 vectors like this:

## Slide 34: Algorithm for best choice of a*, b*, c*
Difference vector clusters are accumulated in a 3D histogram. These vectors represent all candidate reciprocal lattice vectors. For example:
Choose the shortest three linear independent real-space lattice vectors forming a right-handed set.
# COORDINATES OF VECTOR CLUSTER FREQUENCY CLUSTER INDICES
1 -0.0026247 0.0170582-0.0027500 2025. 0.99 -0.00 -0.99
2 -0.0060520-0.0130311 0.0026847 1878. -1.00 0.00 0.01
3 -0.0086356 0.0040538-0.0000834 1832. -0.00 -0.00 -0.99
4 -0.0034720-0.0301176 0.0054258 1536. -1.99 0.00 1.00
5 -0.0052358 0.0342473-0.0054914 1414. 2.00 -0.00 -1.99
6 -0.0015319 0.0195839 0.0114708 1380. 1.00 0.99 -1.00
7 0.0045649 0.0325816 0.0088457 1372. 2.00 1.00 -1.00
. . . . . . . .
60 0.0044282-0.0816564 0.0136375 685. -5.00 -0.00 4.00

## Slide 35: Choose the lattice of highest symmetry and quality of fit<10
LATTICE- BRAVAIS- QUALITY UNIT CELL CONSTANTS (ANGSTROEM & DEGREES)
CHARACTER LATTICE OF FIT a b c alpha beta gamma
* 44 aP 0.0 68.2 68.4 102.9 90.1 90.2 90.1
* 31 aP 0.7 68.2 68.4 102.9 90.1 89.8 89.9
* 33 mP 1.4 68.2 68.4 102.9 90.1 90.2 90.1
* 34 mP 3.2 68.2 102.9 68.4 90.1 90.1 90.2
* 35 mP 3.3 68.4 68.2 102.9 90.2 90.1 90.1
* 32 oP 3.9 68.2 68.4 102.9 90.1 90.2 90.1
* 14 mC 5.5 96.5 96.7 102.9 89.9 90.2 89.8
* 10 mC 6.3 96.5 96.7 102.9 90.1 90.2 90.2
* 13 oC 6.9 96.5 96.7 102.9 89.9 90.2 89.8
* 11 tP 7.6 68.2 68.4 102.9 90.1 90.2 90.1
37 mC 248.2 216.5 68.2 68.4 90.1 90.1 71.8
36 oC 248.9 68.2 216.5 68.4 89.9 90.1 108.2
28 mC 249.2 68.2 216.5 68.4 90.1 90.1 71.8
39 mC 251.8 152.8 68.2 102.9 90.2 90.1 63.6
29 mC 251.8 68.2 152.8 102.9 90.1 90.2 63.6
41 mC 251.9 216.8 68.4 68.2 90.1 90.2 71.6
38 oC 252.4 68.2 152.8 102.9 89.9 90.2 116.4
40 oC 252.6 68.2 216.5 68.4 89.9 90.1 108.2
30 mC 252.9 68.2 216.5 68.4 90.1 90.1 71.8
12 hP 256.1 68.2 68.4 102.9 90.1 90.2 90.1

## Slide 36: Choose the lattice of highest symmetry and quality of fit<10
LATTICE- BRAVAIS- QUALITY UNIT CELL CONSTANTS (ANGSTROEM & DEGREES)
CHARACTER LATTICE OF FIT a b c alpha beta gamma
* 44 aP 0.0 68.2 68.4 102.9 90.1 90.2 90.1
* 31 aP 0.7 68.2 68.4 102.9 90.1 89.8 89.9
* 33 mP 1.4 68.2 68.4 102.9 90.1 90.2 90.1
* 34 mP 3.2 68.2 102.9 68.4 90.1 90.1 90.2
* 35 mP 3.3 68.4 68.2 102.9 90.2 90.1 90.1
* 32 oP 3.9 68.2 68.4 102.9 90.1 90.2 90.1
* 14 mC 5.5 96.5 96.7 102.9 89.9 90.2 89.8
* 10 mC 6.3 96.5 96.7 102.9 90.1 90.2 90.2
* 13 oC 6.9 96.5 96.7 102.9 89.9 90.2 89.8
* 11 tP 7.6 68.2 68.4 102.9 90.1 90.2 90.1
37 mC 248.2 216.5 68.2 68.4 90.1 90.1 71.8
36 oC 248.9 68.2 216.5 68.4 89.9 90.1 108.2
28 mC 249.2 68.2 216.5 68.4 90.1 90.1 71.8
39 mC 251.8 152.8 68.2 102.9 90.2 90.1 63.6
29 mC 251.8 68.2 152.8 102.9 90.1 90.2 63.6
41 mC 251.9 216.8 68.4 68.2 90.1 90.2 71.6
38 oC 252.4 68.2 152.8 102.9 89.9 90.2 116.4
40 oC 252.6 68.2 216.5 68.4 89.9 90.1 108.2
30 mC 252.9 68.2 216.5 68.4 90.1 90.1 71.8
12 hP 256.1 68.2 68.4 102.9 90.1 90.2 90.1
tP
tI
aP
mP
mC
oP
oC
oI
oF
hR
cP
cI
cF
hP

## Slide 37: Integration of intensity for a reflection (image 004)
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
1) Draw boundaries of each reflection
2) Sum the intensities recorded on each pixel within boundary.
3) Repeat for each spot on each image.

## Slide 38: Intensity of this reflection is spread over the first 10 images
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
001 002 003 004 005 006 007 008 009 010
1) Draw boundaries of each reflection
2) Sum the intensities recorded on each pixel within boundary.
3) Repeat for each spot on each image.

## Slide 39: Merging is next

## Slide 40: Output integrated intensities
!UNIT_CELL_CONSTANTS= 67.918 67.918 102.177 90.000 90.000 90.000
! H, K, L, IOBS, SIGMA, XCAL, YCAL, ZCAL, RLP, PEAK,CORR,MAXC,XOBS, YOBS, ZOBS, ALF0,BET0,ALF1,BET1,PSI,ISEG
-47 -11 -7 2.545E+02 2.788E+02 2995.1 2344.0 604.8 1.38699 77.12746 4 33 2978.5 2336.6 605.0 45.91 0.07 -29.44 66.81 -118.54 1
-47 -11 -6 1.002E+03 3.147E+02 22.1 2318.8 94.9 1.39114 78.49145 10 32 29.5 2311.6 95.0 31.25 0.09 -151.27 66.62 95.30 1
-47 -11 -6 1.366E+02 2.771E+02 2994.8 2329.0 603.0 1.39049 79.95720 4 29 2987.3 2329.6 603.1 45.91 0.07 -29.01 66.72 -118.77 1
-47 -11 -5 1.872E+03 3.339E+02 21.5 2304.4 93.7 1.39492 92.47218 23 35 25.3 2304.5 93.7 31.25 0.09 -151.71 66.54 94.48 1
-47 -11 -5 1.204E+03 2.971E+02 2995.5 2314.6 601.1 1.39429 78.44115 15 30 2986.6 2311.4 601.0 45.91 0.07 -28.57 66.64 -118.99 1
-47 -11 -4 6.058E+02 3.242E+02 20.0 2290.6 92.4 1.39900 96.87422 12 77 27.5 2290.6 92.4 31.25 0.09 -152.15 66.47 93.68 1
-47 -11 -4 4.104E+02 2.919E+02 2992.3 2298.0 599.2 1.39845 80.31631 6 31 2982.4 2288.8 598.7 111.48 0.07 -28.13 66.51 -119.18 1
-47 -11 -3 2.735E+03 3.281E+02 17.5 2277.3 91.2 1.40337 95.48840 30 34 19.2 2279.0 91.4 31.25 0.09 -152.59 66.42 92.90 1
-47 -11 -3 9.144E+02 3.109E+02 2994.8 2284.8 597.4 1.40283 75.93009 17 32 2983.7 2282.7 597.4 111.48 0.07 -27.69 66.46 -119.37 1
-47 -11 -2 3.644E+02 2.749E+02 14.1 2264.4 89.9 1.40808 92.92796 6 35 19.6 2264.0 89.8 31.81 0.09 -153.04 66.39 92.13 1 -47 -11 .-47 -11 -1 1.441E+03 2.964E+02 9.7 2252.0 88.6 1.41308 87.63616 23 33 14.4 2252.3 88.7 32.14 0.09 -153.48 66.36 91.39 1
-47 -11 0 3.293E+02 2.450E+02 4.4 2240.0 87.3 1.41836 80.78474 7 31 12.0 2236.6 87.0 32.14 0.09 -153.93 66.36 90.67 1
-47 -10 -9 1.047E+03 3.427E+02 22.3 2316.5 100.7 1.39148 81.59772 16 32 23.3 2318.8 100.7 27.88 0.08 -151.33 66.60 97.62 1
-47 -10 -9 1.153E+02 2.993E+02 2994.5 2326.5 608.7 1.39095 80.67455 4 31 2987.2 2325.2 608.4 45.91 0.07 -28.94 66.70 -116.36 1
-47 -10 -8 4.724E+03 3.767E+02 25.0 2300.6 99.5 1.39410 96.97063 44 49 24.9 2301.0 99.2 31.13 0.08 -151.77 66.48 96.75 1
-47 -10 -8 2.220E+03 3.363E+02 2992.0 2310.8 606.8 1.39349 84.59594 24 33 2988.1 2309.9 606.5 45.91 0.07 -28.51 66.58 -116.63 1
-47 -10 -7 6.914E+03 3.802E+02 26.6 2285.5 98.3 1.39692 99.42799 57 56 29.5 2287.8 98.5 31.25 0.09 -152.20 66.37 95.90 1
-47 -10 -7 3.098E+03 3.250E+02 2990.5 2295.6 604.9 1.39632 86.71242 35 35 2985.3 2294.3 604.7 45.91 0.07 -28.08 66.47 -116.87 1
-47 -10 -6 1.589E+03 2.980E+02 27.3 2271.0 97.1 1.40004 99.54026 16 32 29.5 2272.9 97.1 31.25 0.09 -152.63 66.28 95.07 1
-47 -10 -6 9.778E+02 3.015E+02 2989.9 2281.0 603.0 1.39944 87.42934 11 33 2984.9 2278.8 602.7 45.91 0.07 -27.65 66.38 -117.11 1
-47 -10 -5 1.086E+03 3.186E+02 27.1 2257.0 95.8 1.40345 99.49097 13 33 23.1 2258.3 95.7 31.25 0.09 -153.06 66.20 94.25 1
-47 -10 -5 7.046E+02 3.209E+02 2990.2 2267.0 601.2 1.40285 86.86985 8 33 2986.2 2270.9 601.7 45.91 0.07 -27.22 66.30 -117.33 1
-47 -10 -4 5.056E+03 3.658E+02 25.9 2243.5 94.6 1.40716 99.29475 48 45 27.0 2247.1 94.5 31.25 0.09 -153.50 66.14 93.46 1
-47 -10 -4 2.003E+03 3.387E+02 2986.7 2250.9 599.3 1.40664 89.14124 26 34 2985.0 2252.7 599.2 111.36 0.07 -26.79 66.17 -117.53 1
-47 -10 -3 8.050E+02 3.299E+02 23.8 2230.4 93.3 1.41117 98.79202 16 44 24.0 2225.9 92.9 31.25 0.09 -153.93 66.09 92.69 1
-47 -10 -3 7.560E+02 3.407E+02 2988.8 2237.9 597.5 1.41066 86.07878 7 31 2984.3 2240.7 597.5 111.48 0.07 -26.35 66.12 -117.73 1
-47 -10 -2 3.435E+03 3.298E+02 20.8 2217.9 92.0 1.41550 97.47218 30 44 23.3 2220.1 92.1 31.25 0.09 -154.37 66.05 91.93 1
-47 -10 -2 1.502E+03 3.296E+02 2991.9 2225.3 595.7 1.41499 81.04167 19 38 2987.7 2223.9 595.6 111.48 0.07 -25.91 66.08 -117.92 1
-47 -10 -1 1.185E+03 3.234E+02 16.8 2205.7 90.7 1.42013 94.89558 14 34 23.3 2203.6 91.0 31.25 0.09 -154.81 66.03 91.20 1
-47 -10 0 4.880E+02 3.137E+02 11.8 2193.8 89.4 1.42512 90.43126 12 35 17.5 2193.4 89.6 32.13 0.09 -155.26 66.02 90.47 1
-47 -10 1 7.198E+02 2.775E+02 6.1 2182.4 88.1 1.43037 82.80218 15 34 14.4 2180.9 88.0 32.14 0.09 -155.70 66.03 89.77 1
-47 -9 -11 1.625E+04 5.170E+02 16.5 2302.1 105.2 1.39783 89.53320 83 75 18.8 2303.5 105.5 27.87 0.08 -151.85 66.58 99.11 1
-47 -9 -10 3.139E+03 3.181E+02 21.4 2285.6 104.0 1.39940 97.73439 28 45 23.9 2286.7 104.1 27.87 0.08 -152.27 66.43 98.22 1
-47 -9 -10 1.502E+03 2.902E+02 2994.5 2294.9 610.6 1.39895 79.06115 25 34 2985.4 2292.3 610.5 56.07 0.07 -27.99 66.52 -114.47 1
-47 -9 -9 1.269E+03 3.169E+02 25.2 2269.7 102.8 1.40127 99.12431 15 33 24.9 2272.3 102.7 27.87 0.08 -152.69 66.30 97.34 1
-47 -9 -9 3.660E+02 3.163E+02 2991.9 2279.6 608.7 1.40076 84.73209 6 31 2980.7 2278.0 608.8 45.91 0.07 -27.58 66.40 -114.75 1
-47 -9 -8 3.405E+02 2.993E+02 28.1 2254.4 101.6 1.40342 99.61732 5 36 33.8 2251.4 101.8 27.87 0.08 -153.12 66.17 96.49 1
-47 -9 -8 5.246E+02 3.242E+02 2989.1 2264.3 606.9 1.40292 88.66219 7 31 2979.4 2256.8 606.8 45.91 0.07 -27.15 66.27 -115.01 1
INTEGRATE.HKL file has 1,238,805 lines from this 1.4 Å data set ProK

## Slide 41: Intensity weighted reciprocal lattice, sectioned along c*, cutoff at 8 Å resolution for clarity
L=-12
L=-11
L=-10
L=-9
L=-8
L=-7
L=-6
L=-5
L=-4
L=-3
L=-2
L=-1
L=-0
L=+1
L=+2
L=+3
L=+4
L=+5
L=+6
L=+7
L=+8
L=+9
L=+10
L=+11
L=+12

## Slide 42: Intensity weighted reciprocal lattice, sectioned along c*, cutoff at 8 Å resolution for clarity
L=-12
L=-11
L=-10
L=-9
L=-8
L=-7
L=-6
L=-5
L=-4
L=-3
L=-2
L=-1
L=-0
L=+1
L=+2
L=+3
L=+4
L=+5
L=+6
L=+7
L=+8
L=+9
L=+10
L=+11
L=+12

## Slide 43: Determine the point group symmetry of our intensity-weighted reciprocal lattice.
System | Bravais lattice | Point group | 65 Chiral Space Groups |  |  |  |  | 
Triclinic | P | 1 | P1 |  |  |  |  | 
Monoclinic | P | 2 | P2 | P21 |  |  |  | 
 | C |  | C2 |  |  |  |  | 
Orthorhombic | P | 222 | P222 | P2221 | P21212 | P212121 |  | 
 | C |  | C2221 | C222 |  |  |  | 
 | F |  | F222 |  |  |  |  | 
 | I |  | I222 | I212121 |  |  |  | 
Tetragonal | P | 4 | P4 | P41 | P42 | P43 |  | 
 | I |  | I4 | I41 |  |  |  | 
 | P | 422 | P422 | P4212 | P4122 | P41212 | P4222 | P42212
 |  |  | P4322 | P43212 |  |  |  | 
 | I |  | I422 | I4122 |  |  |  | 
Trigonal/ Rhombo-hedral | P | 3 | P3 | P31 | P32 |  |  | 
 | R |  | R3 |  |  |  |  | 
 | P | 32 | P312 | P321 | P3112 | P3121 | P3212 | P3221
 | R |  | R32 |  |  |  |  | 
Hexagonal | P | 6 | P6 | P61 | P62 | P63 | P64 | P65
 |  | 622 | P622 | P6122 | P6222 | P6322 | P6422 | P6522
Cubic | P | 23 | P23 | P213 |  |  |  | 
 | F |  | F23 |  |  |  |  | 
 | I |  | I23 | I213 |  |  |  | 
 | P | 432 | P432 | P4232 | P4332 | P4132 |  | 
 | F |  | F432 | F4132 |  |  |  | 
 | I |  | I432 | I4132 |  |  |  | 
4
422
Both 4 and 422 can be accommodated by a primitive tetragonal lattice

## Slide 44: What rotational symmetry do you see?
90° rotational symmetry around axis normal to this plane.
L=0

## Slide 45
2-fold rotation around vertical axis
L=0

## Slide 46: How many symmetry copies of this reflection do you see?
3,7,0
L=0

## Slide 47
What are their indices?
L=0
8 symmetry equivalents
3,7,0

## Slide 48
L=0
Is this symmetry consistent with point group 422?
3,7,0
3,-7,0
7,3,0
7,-3,0
-3,7,0
-3,-7,0
-7,3,0
-7,-3,0

## Slide 49
L=0
Reciprocal lattice symmetry operators of point group 422
3,7,0
3,-7,0
7,3,0
7,-3,0
-3,7,0
-3,-7,0
-7,3,0
-7,-3,0
h,k,0
k,h,0
k,-h,0
h,-k,0
-h,-k,0
-k,-h,0
-k,h,0
-h,k,0
point group 422
1) h, k,0
2)-h, k,0
3) h,-k,0
4)-h,-k,0
5) k, h,0
6)-k, h,0
7) k,-h,0
8)-k,-h,0

## Slide 50: The last step in data reduction is merging.
We can improve our estimate of the intensity of reflection h,k,l by averaging (merging) the intensities of all its symmetry-related reflections.
We quantify how well the pattern obeys a certain point group symmetry by calculating Rmerge.
These match
the sym-ops of
point group 422
1) h, k,0
2)-h, k,0
3) h,-k,0
4)-h,-k,0
5) k, h,0
6)-k, h,0
7) k,-h,0
8)-k,-h,0

## Slide 51
j observations of the reflection 30 22 6
<I>= (550 + 500 + 543) / 3
= 531
j | H | K | L | I
1 | 30 | 22 | 6 | 550
2 | -30 | -22 | 6 | 500
3 | 30 | -22 | -6 | 543
Rmerge= S|Ij-<I>|
SIj
Discrepancy
between symmetry related reflections
S|Ij-<I>| = |550-531|+|500-531|+|543-531|
= 19 + 31 + 12
= 62
SIj = 550 + 500 + 543
= 1593
Rmerge = 62/1593 = 0.039 = 3.9%
?
H, K, L=
-H,-K, L=
H,-K,-L

## Slide 52: Point group 4 is a subset of 422.
Point group 4
Point group 422
P4
H, K,L
-H,-K,L
-K, H,L
K,-H,L
-H, K,-L
H,-K,-L
K, H,-L
-K,-H,-L
P422
4-fold symmetry &
perpendicular 2-folds
4-fold symmetry

## Slide 53: If the point group were truly “4”, then Rmerge would be low in point group “4” but high in “422”
Point group 4
Rmerge P4 <20%
Point group 4
Rmerge P422 >50%
Red indicates worst Rmerge outliers

## Slide 54: If the point group were truly “422”, then Rmerge would be low in both “4” and “422”
Point group 4
Point group 422
Rmerge P4 <20%
Rmerge P4<20%

## Slide 55: Merge symmetry-related measurements
Average together intensity values of reflections related by these reciprocal space symmetry operators.
Plane L=0
b*
a*
true?
H, K, L=
-K, H, L=
-H, K, L=
K,-H, L=
K, H,-L=
-H, K,-L=
-K,-H,-L=
H,-K,-L=
Plane L=0
b*
a*
K, H,-L
H,K,L
H,-K, -L
K, -H,L
-K,H,L
-H,-K,L
-H, K,-L
-K,-H,-L
Asymmetric unit of reciprocal space.

## Slide 56
Discrepancy between symmetry related reflections (Rmerge or Rsym) increases with higher resolution. Why?
Shell | Rmerge
100-5.0Å | 0.04
5.0-3.0Å | 0.06
3.0-2.0Å | 0.08
2.0-1.7Å | 0.15
Overall | 0.07
Statistics are analyzed as a function of resolution (N shells).

## Slide 57
CC½ measures the correlation between symmetry-related halves of the unmerged data set.
Shell | CC ½
100-5.0 Å | 0.99
5.0-3.0 Å | 0.99
3.0-2.0 Å | 0.97
2.0-1.7 Å | 0.55
Overall | 0.98
Correlation Coefficient (CC½)
CC½ decreases with increasing resolution.
Diederichs & Karplus say resolution shells with CC ½ > 0.30 have usable information content.

## Slide 58
Average I/s decreases with increasing resolution
Conservatives would say high resolution shells with I/s <2 should be discarded.
Shell | I/sI
100-5.0 Å | 20.0
5.0-3.0 Å | 10.0
3.0-2.0 Å | 7.0
2.0-1.7 Å | 3.0
Overall | 8.2
SIGNAL TO NOISE RATIO (I/s)

## Slide 59
COMPLETENESS?
What percentage of reciprocal
Lattice was measured for a given
Resolution limit?
Better than 90% I hope.
Shell | completeness
100-5.0Å | 99.9%
5.0-3.0Å | 95.5%
3.0-2.0Å | 89.0%
2.0-1.7Å | 85.3%
Overall | 92.5%
Missing wedges of data.

## Slide 60: Prepare a table of data collection statistics & learn to evaluate quality.

## Slide 61: Assignment

## Slide 62: The End